## Slide 1: Logical framework for specifying roof support. Does it suggest alternative approaches to secondary support ?
Ross Seedsman

## Slide 2: Outline
Introduce logical framework
Abridged history of key roof support ideas over the last 30 years
Discussion points
  Negligible horizontal stress at the roof line after the roadway is formed.
  Use simple suspension concepts.
  Never locate bolts or cables near the centreline.
  Stiffness comes at the cost of brittleness.
  Rarely fully grout cables.
  Minimise long tendon support at the development face if you can.
  Revisit trussing.

## Slide 3: Logical framework (Brady and Brown)

## Slide 4: 1970s - High horizontal stresses and numerical stress models
CSIRO (+ ANSI) stress cells – well proven, in rock and coal, precision is +/- 15%.
Continuum finite element methods and IBM PCs make stress modelling easy - we still do not fully understand how rock or coal fails.
Sonic probe extensometers and the height of softening.
Overall compressive failure of roof inferred.

## Slide 5: 1980s – Jointed beams
Roof is jointed and under some compression due to body forces as well as tectonic stresses.
Significance of beam thickness and vertical surcharge on the beam recognised.
Failure by snap-through, crushing, vertical shear, or shear along dipping joints.
Stress “guttering”

## Slide 6: 1990s – Buckling beams
Roof is static or it buckles
Roof line is proposed to be under compression at the development face, maingate, and tailgate.
Poisson’s Ratio effect invoked in the tailgate.
Buckling model leads to;
  High stiffness tendons to middle of roadway.
  Installation close to the face.
What is the evidence ?

## Slide 7: Buckling may look like bending

## Slide 8: Longwall stress redistributions are based on data 5m over rib and 2.5m above the roof line
Data by Winton Gale and SCT

## Slide 9: Elastic theory says the tailgate roof should tend towards tension
The Kirsch (1898) solution (and ALL engineering analyses based on elasticity) says tension in the roof
Application of Poisson’s Ratio effect says compression in the roof
Hint – Poissons Ratio effect applies only if there is complete lateral restraint (uniaxial strain only)
Applied stress

## Slide 10: CSIRO data from Ulan tailgate contrary to Poissons ratio effect
Increases in vertical stress
Decreases in horizontal stress
From Shen et al 2006

## Slide 11: 2002 - Middle Goonyella coal roof suggests tensile roof stresses
Joint and bedding bounded block
No compressive guttering

## Slide 12: 2002 - Tensile roof stresses
Important because the tensile strength of coal and rock masses must be assumed to be zero
When measured, all coal seams report the “anomalous” stress field – all components are compressive, but 0.1 < K < 0.5 .
Stress reductions at roof line result from elevated vertical and reduced horizontal.
Tensile stresses when K < about 0.25.

## Slide 13: Yielding tailgate pillars induce tensile stresses at the roof line
Pillar yield may reduce roof stresses – this is why ALTS works as a pillar design tool.
Bay length of this roof is now longer, horizontal stresses must reduce

## Slide 14: 2005 – Rock Strength Index
Shallow depths and low strength roof rock at Gordonstone, Kestrel and Crinum
Long tendon support needed as a function of both the roof compressive strength and the vertical stress
Rock Strength Index (RSI)=UCS/vertical stress
A return to the idea of overall compressive failure of the roof

## Slide 15: 2007 - Stress measurements at Emerald Mine
Stresses redistributed around softened zone.
Why stress relieving roadways work.
After initial development, negligible imposed horizontal stresses at the roof line. There are some body stresses (jointed beams).
Buckling cannot apply to maingate or tailgate.
From Gale et al, 2007

## Slide 16: 2011 – Recognition of four possible failure modes
SPANNING | PLACE CHANGE/CUT AND FLIT
OMG | FAULTS
BENDING at the roof line | DEVELOPMENT FACES WITH STONE ROOF
COMPRESSIVE FAILURE At or above the bolted horizon | DEVELOPMENT FACES WITH LOW STRENGTH ROOF ROCK MAINGATE CORNERS
RELAXATION At the roof line | DEVELOPMENT ROADWAYS WITH COAL ROOF TAILGATES STRESS NOTCHES

## Slide 17: Maingate corner Compressive failure high in the roof
NEW SOFTENED ZONE
BROKEN ROCK
NEGLIGIBLE CONFINEMENT
Also at the development face with low strength rock (RSI< 3 or there abouts

## Slide 18: Suspension of “softened” zone
Estimate height of softening
  Use extensometry
  Analytical design
    Horizontal to vertical stress ratio at maingate
    Roof Strength Index (UCS/vertical stress)
Assume parabolic fall cavity
Calculate weight
Calculate anchorage length

## Slide 19: A candidate support pattern
Anticipate collapse of the maingate rib corner if longwall face is correctly aligned.
Assume wider, and hence higher, fall zone.
Install at the panel move or over the belt

## Slide 20: Suspension design
Full tensile capacity mobilised
as the side of borehole yields
Load factor : 1.25 – 1.50
Anchorage factor: 2.0-2.5
Block size factor: 1.2
Anchorage (Littlejohn)

## Slide 21: Oblique loading – no reduction in ultimate capacity
Hutchinson and Diederichs, 1996

## Slide 22: Highly stressed fractured ground
“In highly stressed fractured ground, across mobile shear or delamination structures….it is sometimes desirable to reduce the stiffness of the cable bolt system….” (Hutchinson and Diederichs, 1996)

## Slide 23: Point-anchored or fully-grouted long tendons in the coal sector?
Chart: Displacement (mm)
| 0 | 1.137931034500979 | 2.4827586207449044 | 10.13793103460895 | 15.000000000142053 | 18.931034482917127 | 20.89655172433309 | 22.965517241592043 | 24.310344827836015 | 25.758620689866159
Point anchored | 145.6757 | 329.1892 | 442.7027 | 569.4595 | 580.8108 | 594.0541 | 527.8378 | 529.7297 | 368.9189 | 270.5405
Grouted | 5.8659 | 275.6983 | 455.5866 | 551.3966 | 588.5475 | 610.0559 | 619.8324
Clifford et al (2001)

## Slide 24: Why not locate centrally? Why wouldn’t you fully grout?
MORE THAN 6MM OF MOVEMENT INEVITABLE IN THE NEW FAILURE ZONE
RISK ANCHORAGE IS OVERRIDDEN

## Slide 25: Too stiff, too close to the face?
Failure of full grouted cables ?

## Slide 26: Bigger holes give better anchorage in soft rock
STEEL
Grout
UCS = 70MPa
Rock
UCS=30-60 MPa
(The small annulus for bolts relates to the efficiencies of mixing resin cartridges)
Failure will occur at the resin/rock interface

## Slide 27: How much pretension?
Open bedding and joints have no shear resistance.
Arching in fractured rock masses needs closed bedding and joints.
Use sufficient pretension to close the open discontinuities.
Lift at the roof line (mm)
Load in tendon (kN)
RECOMMENDED
PRETENSION

## Slide 28: Tailgate or coal roof Relaxed stresses leading to onset of tension
Anchorage above the relaxed zone
No beam action
Need tensile member
Maingate pattern would give adequate capacity
Mesh panel may not be adequate
Trussing ?

## Slide 29: Summary
Concentrate on strength and ductility before stiffness
For many mines, long tendons are not essential at the maingate. Cheap insurance so long as they do not slow down development.
Design should be based on suspension and anticipate face corner collapse.
When needed, use tensioned, point-anchored long tendons.
(Why not jack the roof up and install passive grouted plain strand cable ?)
Long tendons (or standing support) needed in tailgate if pillars are designed to yield.
More consideration needed on restraint at the roof line.