## Slide 1
ACARP – Roadway Development Operators Workshop, October 2011

## Slide 2: Long Tendon System Designed for Roadway Development
  1998: Jennmar partnered with Springvale coal in developing one of the first 8m long tendon systems for high volume installation off the continuous miner. The mine has been installing such a system throughout most of the development roadways since 1998, the mine installs over 1000 x 8m cables per month.
  Jennmar has built on this experience over the last decade and has partnered with many other mines in implementing mid to long tendons installed off the miner – This presentation shares some of the lessons we have learned along the way…..

## Slide 3: The step changes
  1998: development of the post groutable Bulbed Superstrand, large diameter 36mm resin capsules, tensioners running off the miner hydraulics, grout tubes inserted alongside the cable.. Point anchored and tensioned off the miner with grouting outbye as required
  2000: Point anchored pre-tensioned SuperStrand off the miner becomes a common choice for intersections after QLD roof fall incident
  2003: development of the 4m full resin encapsulated SuperStrand. Same bit as roof bolts, roof bolt resin at the top, XXS low viscosity resin at the bottom. Only suitable for seam heights of >3m as 2.5m of resin capsules were being inserted
  2007: development of the hollow strand with flexible centre tube. Smaller diameter hole and no tubes to become pinched off with roof movement. Point anchored and tensioned off the miner with grouting outbye as required
  2009 : development of the ToTo threaded tensioning device for cables to eliminate hydraulic tensioners

## Slide 4: DESIGN FOCUS ON THE “Operator”
  The system must be able to be installed by the full skill range of operators
  The current state of skills shortage has led Jennmar to keep designs as simple as possible with minimal components and installation steps
  At the same time an aged workforce is dispersed amongst new starters and the design must focus on minimising manual handling – perfect example is the Lobster Cable Pusher
  Its no use having the highest capacity, highest performance cable bolt in the support plan when quality installation by the average face operator can not be guaranteed
  Ground control can be compromised if a system design makes it too difficult for operators to install correctly

## Slide 5: THE BIG PICTURE
  Before discussing some Jennmar products built around our “focus on the Operator” approach, there are some bigger picture issues which the next few slides will discuss, these are;
  Packaging
  Standardisation
  Training

## Slide 6: Packaging
  Where possible;
  Minimise labour required to un-pack tendons. Eg straight tendons, all facing one way
  Minimise labour in assembling components . Eg End fittings attached to cable, in built-grout/breather tubes, in-built grout adaptor
  Packaging must have added safety due to more personnel exposed within the confinement of a development heading. Eg plastic strapping, rounded corners on trays, QDS duck bills purpose built
  Clear identification of components is critical to ensure operators do not mix up with primary support products. Eg resin labels, different colour coding

## Slide 7: Standardisation
  Where possible ;
  use the same drill bit, plate, resin and dolly as primary support products to minimise ‘operator error’. Eg Introducing a 28mm bit for tendons will lead to using 28mm bits with primary support where the design may be 27mm bits.
  Where possible use the same tendon components as used outbye Eg Same diameter cables throughout the same mine means only one tendon tensioner , B&W and mixing dolly on site.
  Different sized cables can lead to incorrect B&W and tensioners being used on cables which poses a major safety hazard of slipping end fittings, falling tensioners.

## Slide 8: Training
  Typically mines only start installing tendons off the miner when they have to -TARP driven and/or bad roof
  The large number of operators across all 24/7 shifts need intense training with theory and UNDERGROUND supervision to ensure the tendons will be installed correctly to control the almost certain roof displacement

## Slide 9: Jennmar Products & Applications
  The following slides detail the two main Jennmar tendon systems that are design focused for Roadway Development
  Hollow TG cables - post groutable 4 m – 10 m
  SuperStrand ToTo cables – resin anchored 4m – 8m

## Slide 10: Hollow TG Cable
In-built central grout tube
Resin anchored
Post-grouted top-down
Bulbed resin anchorage
Grouted section
The black plastic cap protects the grout tube from being blocked by mud/dirt during dragging through the mud etc

## Slide 11: Hollow TG Cable
In-built central grout tube allows smaller 42mm drill hole
  High bond strength to the rock
  Only 1 x 800mm resin required to achieve >55t point anchor
NO reaming of the hole
Flexible hollow tube makes it the easiest post groutable cable to manually handle
Plate has 46mm hole, allows drilling and resin insertion through the plate
Barrel & wedge comes attached to the cable
Lightweight hydraulic tensioners available, with the ToTo device being developed for the hollow strand
Weight 2.8 kg/m compared to 2.5 kg/m of the superstrand

## Slide 12: SuperStrand ToTo
  Elimination of hydraulic tensioners to minimise hydraulic injection exposure for the “operator”
  No reaming of the hole is required – safer in mesh & faster
  No exposed components that can fall off or be affected by the environment
  Internal anti-friction system – stays intact and free of contamination, and can withstand full system loading without failure
  Stubbie ToTo (160mm long), standard ToTo (220mm)
  Not affected by head frame as all tensioning processes are beneath the drill mast

## Slide 13: ToTo Specifications
Diameter | Number of wires | Steel Area | Typical Yield Strength | Typical Breaking Load |  | Elongation at Failure
 |  |  |  |  | at B&W | 
21.8 mm | 19 | 313 mm 2 | 525kN (53 Tonne) | 590kN (60 Tonne) | 52 Tonne | 6 –7 %
Outside bush which enables rotation to be applied to the fitting to achieve cable tension. The maximum diameter of the outside bush is less than 75mm to enable passing of the end fitting through gripper jaws on bolting rig head plates.
Computer aided design achieves most efficient materials and thickness to minimise weight.
Special tightening spanner designed to take high torque loads and pass through gripper jaws -supplied by Jennmar

## Slide 14: Tiger Dolly Specifications
Recommend maximum torque applied to the locking square drive = 725 N.m
Shaft and socket components well within maximum design torque of 1800 N.m

## Slide 15: ToTo Installation

## Slide 16: Tensioning with Tiger Dolly

## Slide 17: Automated Push Button Bolting Rigs
Semi and fully Automated drill rigs
Some automated bolters only have one program, and that’s for roof bolts. No push button feature is currently available for cable installation
The installation process has totally changed with the fully encapsulated 4m cable system
Semi automated rigs - the operator has much more control and is similar to manual levers
Operator involvement in creating procedures and risk assessments is a must

## Slide 18
THE ISSUES WITH SOME NEW BOLTING MACHINES
Drill pot positioning: Some new machines have raised the drill pot to protect hydraulic hoses.
Higher drill pots have created problems installing 4 metre fully encapsulated cables
When using fully encapsulated systems 2500mm of resin is used to give the maximum encapsulation of the system. Therefore, 2700mm of cable protruding from the roof must fit into the dolly at the drill pot.
With the new Automated push button bolters, it was found that operators had major issues with cables including;
  Manual handing due to pushing cable into resin
  Gloving due to pushing cable into resin
  Less control of thrust meant more potential cable whip when mixing through 2500mm of resin

## Slide 19: Jennmar initiative with equipment changes to drill pot height
Jennmar wanted to reduce the length of resin while keeping the same volume to minimise the majority of installation issues.
JLOK resins created a special twin capsule in a 26 mm diameter. The same volume of resin but 300mm shorter than old system.
Jennmar minimised the fast set portion and increased the Extra Slow portion to enable longer spinning for operators.
A longer pre-tensioned beam is created
Tensioning is performed immediately like a roof bolt when the short fast set is at the top
Zip ties are being eliminated to minimise hydraulic lock

## Slide 20: Correct drill steel length
The “Change Management” with the introduction of a new bolting rig ‘MUST’ consider different length drill steel across the whole mine
Mine sites should take the time to set up the correct length drill steels to eliminate over and under drill issues
Correct drill bits
Jennmar 21.8mm Superstrand allows use of 27mm or 28mm drill bits to enable standardisation with any site roof bolt bits
This allows no mix up of roof bolt and cable bolt drill bits and vice versa
A 1mm increase in drill bit can reduce bond strength by 20%

## Slide 21: Gripper Jaws
To ensure cables are installed as safely as possible, the use of the timber jack and gripper jaws should always be utilised on the side of safely
Lowering the timber jack with the grippers closed around the cable will keep the cable stiff for thrusting into the long resin capsule.
If the volcano plate is sitting on the head plate, the grippers holding the cable will prevent the plate being dislodged
Grippers allows thorough rotation and controlled thrust to safely install fully encapsulated cables

## Slide 22: Thanks for your attention For further information: Tim Gaudry – tgaudry@jennmar.com.au Peter Craig – pcraig@jennmar.com.au ANY QUESTIONS ??